## Slide 1: A Series on Design Considerations for Small-Scale Wind Turbines
Elan Fullmer, M.S.
May 7th, 2025
Part 4: Rotor Solidity
Department of Mechanical & Aerospace Engineering
Syracuse University

## Slide 2
Table of Contents
Why Small-Scale Wind?
Design Parameters Under Investigation
Background I. Defining Rotor Solidity
Background 2. Defining Tip Speed Ratio
Motivation
Research Objective & Method
Experiment Definition
Testing Setup I. Facilities
Testing Setup II. Apparatus in Detail
Rotor Design I. Experimental Constraints
Rotor Design II. Blade Fabrication
Rotor Design III. Comparison 1
Rotor Design IV. Comparison 2
Results & Discussion

## Slide 3
Solar Panels
Why Small-Scale Wind?
Accessibility to on-site power
  Residential/agricultural
  Commercial/industrial
  Disaster relief
  Construction applications
  Military sites
Supplement to solar power (for overnight and in winter)
Project Goal:
Improve viability of small-scale wind by investigating design parameters for HAWTs
( Horizontal Axial Wind Turbines)
‘Small-Scale Wind’ is defined here as a wind turbine with a generation capacity of less than 10kW.
Figure (1): [1]

## Slide 4: Design Parameters Under Investigation
1. Yaw Motion Control
2. Ducting and Diffusion
3. Twist Optimization & Pitch Control
7. Material & Manufacturing
6. Structure & Sizing
5. Blade Sweep
4. Rotor Solidity
3

## Slide 5: Background I. Defining Rotor Solidity
Research Objective & Method
Background II
Background I
Motivation
Rotor solidity is defined as the ratio of blade area to swept area for a given stage.
  Function of number of blades
  Function of chord length
  Function of the angle of twist
High Solidity
Low Solidity
r – Radius at a given stage
– Number of blades
– Twist angle
– Chord
Chord
Figure (2): [2]
Figure (3): [3]

## Slide 6: Background II. Defining Tip Speed Ratio
Tip Speed Ratio (TSR, or ) is essentially a measure of the blade’s tip speed.
– Tip blade velocity
– Free stream wind speed
– Radius at the tip
– Rotational velocity
Large Radius
High TSR
Low Solidity
Small Radius
Low TSR
High Solidity
Utility-Scale Wind Turbine
Small-Scale Wind Turbine
Background I
Background II
Motivation
Research Objective & Method

## Slide 7: Motivation
Low solidity rotors are less efficient but can operate at higher TSR’s, achieving higher power generation if the rotor size is large.
High solidity rotors are more efficient at lower TSR’s, but lack operational range, achieving higher power generation if the rotor size is small.
Zawadzki, Karol & Smiechowicz, 2021 [4]
Conclusion: Opposed to the utility scale, small-scale wind turbines should have high solidity rotors to maximize economic viability.
Figure (4): Shows an increase in power coefficient (efficiency) at lower TSRs with an increase in the number of blades (solidity).
Background I
Background II
Motivation
Research Objective & Method
  Higher solidity will allow for higher power efficiency with a smaller rotor.
  Small turbines can be feasibly manufactured with higher solidity while maintaining structural integrity and low material cost.

## Slide 8: Research Objective & Method
Motivation
Method:
Background I
Background II
Experimentally determine how the distribution of solidity along the blade affects the power generated. Experimentally verify the relationship between rotor solidity, TSR, and power efficiency.
Design and construct the wind turbine test system.
Utilize the testing system to obtain results.
Experiment Definition
Define the experiment and expected outcomes.
Testing Setup
Rotor Design
Design the wind turbine rotors of varying solidity.
Results & Discussion
Objective:
Research Objective & Method
Notes: Redesign this slide

## Slide 9: Experiment Definition
Testing Setup
Experiment Definition
Rotor Design
Comparison 1: Verify the relationship between rotor solidity, TSR, and power efficiency.
Comparison 2: Determine how the distribution of solidity along the blade affects the power generated.
Rotor 1 –
Low Solidity
Rotor 2 –
High Solidity
  Expected Outcome:
  Rotor 1 will show higher operational range of TSR’s.
  Rotor 2 will show higher power efficiency at lower TSR’s.
Rotor 2 –
Root-Weighted Solidity
Rotor 3 –
Tip-Weighted Solidity
(Same average solidity as Rotor 2)
  Expected Outcome:
  Rotor 3 will show an overall higher power efficiency, due to an increase in power production at the tip, and decreased blockage at the root.
Results & Discussion

## Slide 10: Testing Setup I. Facilities
Testing Setup
Experiment Definition
Rotor Design
  Figure [6]: Diagram of the closed-loop subsonic wind tunnel
  Figure [5]: Assembled testing setup in the wind tunnel, utilizing a digital rotary torque sensor and a friction disc brake.
Subsonic closed-loop wind tunnel
2’ 2’ test section
Reynolds Number ~ 262,941 at the tested wind speed of 6.5 m/s (turbulent flow)
Friction Disc Brake
Digital Rotary Torque Sensor
Steel ‘Spine’ Blade Housing
Results & Discussion
Notes: Redesign this slide

## Slide 11: Rotor Design I. Experimental Constraints
Testing Setup
Experiment Definition
Rotor Design
Tunnel Blockage
  Maximum blockage of 25% to mitigate boundary effects [5]
  Results in:
    Swept area of 1 ft2
    Radius of 6.78 inches (172 mm)
Operational Speed
  Given:
    Wind speed of 6.5 m/s
    Desired TSRmax of 2
    Radius of 0.172 m
  Requires operation of up to 600 RPM
Structural Integrity
  Material: PLA plastic
  Additively manufactured (FDM)
  Danger of structural failure at high speeds
Solution
4 ft2
1 ft2
– rotational velocity in rad/s
  Figure (13): Initial blade prototype, showing material failure at the root. 80% infill with honeycomb grid structure.
  ‘Steel spine’ for structural strength
  Blades are 3D printed with ¼” shaft housing
  Figure (14): Steel spine assembled in wind tunnel (left). Cross sectional diagram of blade model, showing shaft housing (right).
Results & Discussion
Notes: Redesign this slide

## Slide 12: Rotor Design II. Blade Fabrication
Method:
All rotors are based on NREL 5MW wind turbine geometry [6]
Blades were created using Qblade, an open-source wind turbine design software.
Twist is consistent between rotors, re-optimized from the original geometry for a TSR of 1 using Qblade’s Blade Element Moment Theory
Rotor 1: ½ cut of original blade, re-optimized and scaled to 6.78 in
All rotors should be aerodynamically similar in efficiency to isolate the effects of rotor solidity.
Rotor 2: ⅓ cut of original blade, re-optimized and scaled to 6.78 in
Rotor 3: Same as rotor 2, with a different chord distribution
Original NREL 5MW blade geometry, 207 ft length
DU40_A17
DU35_A17
DU30_A17
DU25_A17
DU21_A17
NACA64-618
Airfoil ID:
Testing Setup
Experiment Definition
Rotor Design
Results & Discussion
Notes: Redesign this slide

## Slide 13: Rotor Design III. Comparison 1
Rotor 1:
Rotor 2:
Chart: Rotor #1 Solidity Distribution
| 1.36 | 1.704 | 2.048 | 2.7370000000000001 | 3.0739999999999998 | 3.411 | 4.0860000000000003 | 4.76 | 5.4349999999999996 | 6.11 | 6.7839999999999998
 | 0.67284 | 0.58726 | 0.51875 | 0.41923 | 0.37529 | 0.3385 | 0.2806 | 0.23706 | 0.20367 | 0.17636 | 0.15457
Chart: Rotor #2 Solidity Distribution
| 1.5529999999999999 | 2.0830000000000002 | 2.6120000000000001 | 3.6709999999999998 | 4.1900000000000004 | 4.7089999999999996 | 5.7460000000000004 | 6.7839999999999998
 | 0.95454 | 0.78296 | 0.6585 | 0.49738 | 0.43526 | 0.38549 | 0.31117 | 0.25195
Average solidity,
Constant chord distribution
“Traditional” inverse solidity distribution
Average solidity,
Constant chord distribution
“Traditional” inverse solidity distribution
Testing Setup
Experiment Definition
Rotor Design
Results & Discussion
  Figure (16): Assembled Rotor 1 with spine
  Figure (18): Assembled Rotor 2 with spine
  Figure (15)
  Figure (17)
Notes: Redesign this slide

## Slide 14: Rotor Design IV. Comparison 2
Rotor 2:
Chart: Rotor #2 Solidity Distribution
| 1.5529999999999999 | 2.0830000000000002 | 2.6120000000000001 | 3.6709999999999998 | 4.1900000000000004 | 4.7089999999999996 | 5.7460000000000004 | 6.7839999999999998
 | 0.95454 | 0.78296 | 0.6585 | 0.49738 | 0.43526 | 0.38549 | 0.31117 | 0.25195
Average solidity,
Constant chord distribution
“Traditional” inverse solidity distribution
Rotor 3:
Average solidity,
Linear chord distribution
Constant solidity distribution
Chart: Rotor #3 Solidity Distribution
| 1.5529999999999999 | 2.0830000000000002 | 2.6120000000000001 | 3.6709999999999998 | 4.7089999999999996 | 5.7460000000000004 | 6.7839999999999998
 | 0.50065 | 0.50307 | 0.50002 | 0.49147 | 0.48437 | 0.47826 | 0.46875
Results & Discussion
Testing Setup
Experiment Definition
Rotor Design
  Figure (18)
  Figure (20): Assembled Rotor 3 with spine
  Figure (17)
  Figure (19)
Notes: Redesign this slide

## Slide 15: Results & Discussion I.
Results & Discussion
Testing Setup
Experiment Definition
Rotor Design
Chart: Comparing Power Curves of Rotors 1-3
| 0.48107404111089191 | 0.64707885617742122 | 0.68816769484452611 | 0.79920814289498576 | 0.83329206874640149 | 0.99293615215271958 | 1.0036910797485035 | 1.0465993401047398 | 1.1826519604420782 | 1.1886145368811916 | 1.2905634489873394 | 1.3873299348426698
Blade 1 | 0.013251 | 0.022166 | 0.018412 | 0.018229 | 0.022312 | 0.024 | 0.026043 | 0.025335 | 0.022783 | 0.021534 | 0.016524 | 0.0084642
Blade 2 | 0.018651 | 0.021168 | 0.033265 | 0.038703 | 0.041996 | 0.046184 | 0.043499 | 0.048765 | 0.045289 | 0.047439 | 0.04767 | 0.044329 | 0.041822 | 0.025833 | 0.031241 | 0.0042351
Blade 3 | 0.0062296 | 0.024086 | 0.017359 | 0.03132 | 0.024688 | 0.062505 | 0.066049 | 0.059936 | 0.06293 | 0.059359 | 0.064101 | 0.052039 | 0.048982 | 0.0587 | 0.053762 | 0.062347 | 0.052643 | 0.052744 | 0.032353 | 0.042931 | 0.046183 | 0.04564 | 0.044843 | 0.018956 | 0.029979 | 0.033944 | 0.022014
avg = 0.36
R2 = 0.88
TSRopt = 1.01
Cpmax = 0.025
avg = 0.53
R2 = 0.94
TSRopt = 1.06
Cpmax = 0.046
avg = 0.49
R2 = 0.82
TSRopt = 1.09
Cpmax = 0.060
  Trend lines use a cubic power curve model[7]
Rotor 1:
Rotor 2:
Rotor 3:
  Figure (21)

## Slide 16: Results & Discussion II.
Results & Discussion
Testing Setup
Experiment Definition
Rotor Design
Rotor 1 had the lowest efficiency of the three, as expected.
Increasing the average solidity by 50% led to an 84% increase in efficiency in Rotor 2 compared to Rotor 1.
Rotor 2 saw an increase in operational TSR compared to Rotor 1, contrary to expectations.
Rotor 1
Rotor 2
Rotor 3
Summarized Results
Comparison 1:
Rotor 3 outperformed Rotor 2, as expected.
Rotor 3 achieved a 34% increase in efficiency compared to Rotor 2, despite a slight decrease in average solidity, by shifting the solidity distribution toward the blade tip.
Comparison 2:
  Figure (21)
Notes: Redesign this slide

## Slide 17: Results & Discussion III.
Results & Discussion
Testing Setup
Experiment Definition
Rotor Design
Conclusion: Results show great potential for more efficient small-scale wind turbines through strategic rotor solidity manipulation.
Increasing rotor solidity is strongly related to an increase in power production for a TSR near 1.
  This experimentally validates a theoretical study on vertical axial wind turbines performed by Ghiasi & Najafi in 2022, where they determine the upper limit on this phenomena [8].
Rotors with a constant solidity distribution will significantly outperformed rotors with an inverse solidity distribution
  Future work includes an analysis on solidity distribution with a positive radial gradient, more strongly weighted toward the tip of the blade.
Notes: The low solidity rotor tested in this experiment did not show an increase in operational TSR when compared to the higher solidity rotors. This could be due to a lack of aerodynamic similarity between the models
The low Cp (0.02-0.06) found in this study is assumed to be a product of the prototype-scale model and is speculated to increase for a life-sized prototype.

## Slide 18: References
Thank you!
Special Thanks to:
Dr. Jackie Anderson – Faculty Advisor
Sydney Jud and Kendra Miller
SU-ECS Machine Shop
SU MakerSpace
[1] https://www.checkatrade.com/
[2] https://www.windpowermonthly.com/article/1460680/vestas-edpr-install-single-converter-wind-solar-hybrid
[3] https://www.rockridgewindmills.com/our-windmills/windmill-tower-sizes/
[4] Zawadzki, Karol & Smiechowicz, Wojciech & Lipian, Małgorzata & Baszczyńska, Anna & Tarkowski, Michał. (2021). Influence of the Solidity Ratio on the Small Wind Turbine Aerodynamics. E3S Web of Conferences. 242. 03006. 10.1051/e3sconf/202124203006.
[5] T.Y. Chen, L.R. Liou, Blockage corrections in wind tunnel tests of small horizontal-axis wind turbines, Experimental Thermal and Fluid Science, Volume 35, Issue 3, 2011, Pages 565-569, ISSN 0894-1777, https://doi.org/10.1016/j.expthermflusci.2010.12.005.
[6] https://github.com/old-NWTC/FAST/blob/master/CertTest/5MW_Baseline/Airfoils/DU21_A17_coords.txt
[7] C. Carrillo, A.F. Obando Montaño, J. Cidrás, E. Díaz-Dorado, Review of power curve modelling for wind turbines, Renewable and Sustainable Energy Reviews, Volume 21, 2013, Pages 572-581, ISSN 1364-0321
[8] Ghiasi, P., Najafi, G., Ghobadian, B., Jafari, A., & Mazlan, M. (2022). Analytical Study of the Impact of Solidity, Chord Length, Number of Blades, Aspect Ratio and Airfoil Type on H-Rotor Darrieus Wind Turbine Performance at Low Reynolds Number. Sustainability, 14(5), 2623.