## Slide 1: Thermo-mechanical analysis of a computer CPU cooling system Finite Element Analysis 12.16.2024 Elan Fullmer

## Slide 2: Problem Definition
As it can be seen in Figure(2), heat sink is made of aluminum, while the fan and the fan-casing are made of glass-filled nylon. The motor that drives the fan is assumed to be an integral part of the fan and it is assumed to be made from same material as the fan.
Determine the steady-state thermal response and structural stresses associated with the following cooling system:
Figure (1)
Figure (2)

## Slide 3: Material Properties
Young's Modulus | 
6.2e+09 | Pa
Coefficient of Thermal Expansion | 
2.56e-05 | 1/°C
Tensile Yield Strength | 
5.5e+07 | Pa
Isotropic Thermal Conductivity | 
0.23 | W/m·°C
Poisson's Ratio | 
0.35 | 
Density | 
1360 | kg/m³
Density | 
2700 | kg/m³
Young's Modulus | 
6.98e+10 | Pa
Poisson's Ratio | 
0.33 | 
Coefficient of Thermal Expansion | 
2.36e-05 | 1/°C
Tensile Yield Strength | 
2.76e+08 | Pa
Isotropic Thermal Conductivity | 
167 | W/m·°C
Glass Filled Nylon
Aluminum

## Slide 4: Part 1 Steady State Thermal Response

## Slide 5: Model and Mesh
# of Elements: 299472
Max Skewness: 0.99997
Only ~1,500 elements with skewness over 0.99
Figure (3): Model as visualized in Ansys SpaceClaim.
Figure (4): Full-body mesh visualization.

## Slide 6: Boundary Conditions, Steady State Thermal
Initial Temperature for entire body is 22 degrees C.
Heat source of 2000 W/m2 (A).
Convection is induced by the fan with ambient air at 28 oC, and a convective heat transfer coefficient of 30 W/m2 oC (B).
Figure (5): Boundary conditions A & B are applied.
Figure (6): Boundary condition A shown in detail.

## Slide 7: Results, Full Body
Temperature Contour Plot
Heat Flux Contour Plot
Figure (7): Full-body temperature contour.
Figure (8): Full-body heat flux contour.

## Slide 8: Temperature Contour Plots, Individual Components
Heat Sink
Fan Housing
Fan
Figure (9): Temperature contour of the heat sink.
Figure (10): Temperature contour of the fan housing.
Figure (11): Temperature contour of the fan.

## Slide 9: Heat Flux Contour Plots, Individual Components
Heat Sink
Fan Housing
Fan
Figure (12): Heat flux contour of the heat sink.
Figure (13): Heat flux contour of the fan housing.
Figure (14): Heat flux contour of the fan.

## Slide 10: Discussion I
There is a quick dissipation of heat between the aluminum heat-sink and the plastic case due to the low thermal conductivity of nylon, acting as an insulator.
Very little heat transfers to the fan components, providing the ability to use materials with a relatively high thermal expansion, without possibility of interference with the fan housing. More on this in Part 2
Local maxima of heat flux can be found at the interface between the heat sink and housing as seen in Figure(12). This phenomena is explained by the steep temperature gradient between the sink and housing seen in Figure(7).

## Slide 11: Part 2 Full Body Thermal-Structural Analysis

## Slide 12: Boundary Conditions, Thermal-Structural
Figure (15): Boundary condition A is applied
Figure (16): Boundary condition B is applied
Stress and deformation of the entire body is analyzed under the previously defined thermal loading in addition to the mechanical effects of the fan’s rotation.
Fixed Support at heat source (A).
Fan component is rotating at a speed of 524 rad/s (5000 rpm) (B).

## Slide 13: Results, Full Body
Von-Mises Stresses
Total Deformation Contours
Figure (17): Full body Von-Mises stress contours view 1.
Figure (18): Full body Von-Mises stress contours view 2.
Figure (19): Full body total deformation contours view 1.
Figure (20): Full body total deformation contours view 1.

## Slide 14: Von Mises Plots, Individual Components
Heat Sink
Fan Housing
Fan
*Von Mises stresses are represented by a log scale
Figure (21): Heat sink Von Mises stress contours.
Figure (22): Fan housing Von Mises stress contours.
Figure (23): Fan Von Mises stress contours.

## Slide 15: Total Deformation Plots, Individual Components
Heat Sink
Fan Housing
Fan
Figure (24): Heat sink total deformation contours.
Figure (25): Fan housing total deformation contours.
Figure (26): Fan total deformation contours.

## Slide 16: Safety Factor Contours, Individual Components
Heat Sink
Fan Housing
Fan
Conclusion:
Heat sink has the highest risk of structural failure.
Lowest safety factor is 1.64, meaning the CPU cooling system will not have structural failure during operation.
Figure (27): Heat sink stress safety factor.
Figure (28): Fan housing stress safety factor.
Figure (29): Fan stress safety factor.

## Slide 17: Radial Deformation of Fan Component
Geometrical distance between fan and housing: 5.76mm
Maximum radial deformation of fan: 0.0762 mm
Conclusion: There is ample clearance between the fan and the housing.
Figure (30): Fan radial deformation contours.

## Slide 18: Part 3 Periodic Structural Analysis of Fan

## Slide 19: Model and Mesh
# of Elements: 569418
Max Skewness: 0.91631
1/7th periodic sector of fan
Material: Glass Filled Nylon
Figure (31): Fan blade periodic section geometry.
Figure (32): Fan blade periodic section mesh.

## Slide 20: Boundary Conditions, Periodic Structural
Figure (33,upper & 34,lower): Periodic section defined.
Figure (35): Fixed support defined.
Figure (36): Rotation of 5000rpm is defined.

## Slide 21: Results, Periodic Structural I
Von Mises Stress
Total Deformation
Figure (37): Total deformation contours of fan section.
Figure (38): Von Mises stress contours of fan section.

## Slide 22: Results, Periodic Structural II
Safety Factor
Radial Deformation
Figure (39): Radial deformation contours of fan section.
Figure (40): Safety factor of fan section.

## Slide 23: Discussion II
The temperature load present in part 1 & 2 had little effect on the stresses of the fan component. This is due to the low thermal conductivity of the fan housing
Deformation of the fan component was about 0.02mm smaller without the addition of thermal loading.
The similar results shown in part 3 serves as validation of the quality of the mesh for part 1 & 2.

## Slide 24: Parametric Analysis of Fan Rotational Velocity
RPM | Maximum Total Deformation (mm) | Maximum Von Mises Stress (MPa) | Safety Factor (max of 15)
1000 | 0.00265 | 0.303 | 15
2000 | 0.0106 | 1.211 | 15
3000 | 0.0239 | 2.724 | 15
4000 | 0.0425 | 4.843 | 11.4
5000 | 0.0663 | 7.567 | 7.3
6000 | 0.0955 | 10.90 | 5.0
7000 | 0.130 | 14.83 | 3.7
8000 | 0.170 | 19.37 | 2.8
9000 | 0.215 | 24.52 | 2.2
10000 | 0.265 | 30.27 | 1.8
Periodic Structural Analysis of Fan, Cont.
Table (1): Parametric analysis of varying RPM values for the structural analysis of the fan. Highlighted portion shown the original simulation results of 5000 rpm

## Slide 25: RPM vs Maximum Von Mises Stress
Chart: RPM
| 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000
 | 0.30267 | 1.2107 | 2.7241 | 4.8428 | 7.5669 | 10.8963 | 14.831 | 19.3712 | 24.5166 | 30.2674
The relationship between RPM and Maximum Stress is quadratic.
This relationship comes from the following equations:
Equation of Centrifugal Force
F = mv² r
F – Force
m – mass
v – velocity
r - radius
Equation of Stress
σ = F / A
σ - Stress
A – Area
So, stress is proportional to velocity squared.
Figure (41): Plotted parametric analysis of RPM vs. Stress for fan component

## Slide 26: Minimum Safety Factor of 1.5
With the fan running at 11,000 rpm, the minimum safety factor is ~1.5
Maximum Deformation is still under 5.76mm, so the fan will not interfere with the housing.
Results at 11,000rpm:
RPM | Maximum Total Deformation (mm) | Maximum Von Mises Stress (MPa) | Safety Factor (max of 15)
11000 | 0.321 | 36.62 | 1.502
 | Maximum Radial Deformation (mm) |  | 
 | 0.304 |  | 
 | Maximum Axial Deformation (mm) 0.017 |  | 

## Slide 27: Part 4 Modal Analysis of the Fan Component

## Slide 28: Model and Mesh
# of Elements: 155777
Max Skewness: 0.99956, ~330 over 0.99
Figure (42): Geometrical model of fan component.
Figure (43): Mesh of fan component.

## Slide 29: Boundary Condition
Figure (44): Fixed support for modal analysis of fan.

## Slide 30: Results: Natural Frequencies
1. 433.95 Hz
2. 1070.6 Hz
3. 1070.7 Hz
4. 1262.8 Hz
5. 1263. Hz
6. 1366.1 Hz

## Slide 31: Mode shape Deformation Contours
Mode 1
Mode 2
Mode 3
Figure (45)
Figure (46)
Figure (47)

## Slide 32
Mode shape Deformation Contours cont.
Mode 4
Mode 5
Mode 6
Figure (48)
Figure (49)
Figure (50)